## Slide 1
Attitude estimation with Extended Kalman Filter
Mirko Mazzoleni
Corso di IDENTIFICAZIONE DEI MODELLI E ANALISI DEI DATI
A.A. 2018/2019

## Slide 2: Outline
Introduction
Model
Preprocessing and implementation of EKF

## Slide 3: Outline
Introduction
Model
Preprocessing and implementation of EKF

## Slide 4: Scope of the laboratory
Use the Kalman Filter to perform attitude estimation of a smartphone, using inertial platform measurements:
    Gyroscope
    Accelerometer
    Magnetometer
LPT: Access SAMSUNG smartphone sensors with the combination: *#0*#
    Reference  Orientation Estimation using Smartphone Sensors – Linkoping university

## Slide 5: Frames
We will use two coordinate systems: the world frame and the sensor frame
These coordinate systems are related via linear transformations
    Reference  Robotica: modellistica, simulazione e controllo
    Siciliano, Sciavicco, Villani, Oriolo
where is a point expressed in the sensor frame and is the same point expressed in the world frame
The relative rotation between the two frames is given by , the rotation matrix
Since we consider only rotation, the term is discarded

## Slide 6: Frames
The world frame is fixed
The sensor frame rotates
and express the point coordinates in the two frames
The focus of this lab is to estimate the rotation 𝑅^(𝑊/𝑆) based on the sensors measurements available from a smartphone
By estimating 𝑅^(𝑊/𝑆) we are able to obtain the object attitude in the fixed frame

## Slide 7: Frames
A rotation matrix has 3 meanings
Gives the orientation of one set of coordinates with respect to another
Represents a transformation of coordinates that relates the coordinates of the same point in two different frames
Is the operator which rotates a vector in the same frame

## Slide 8: Attitude representation
An object attitude can be expressed via rotation matrices (9 elements)
The 9 elements are not independent because of orthogonality constraints  3 indenpendent parameters (3 angles)
Euler angles
ZYZ representation (current frame)
RPY representation (fixed frame)
PROBLEM: Singularities
Different positions in the same have the same representation

## Slide 9: Quaternions
Non minimal representation (4 parameters) but with no singularities
Represent a rotation of an angle 𝛼 around the axis ,
We have that and represent the same rotation. So the representation of a rotation must be chosen according to the specific application

## Slide 10: Rotation matrix corresponding to a quaternion

## Slide 11: Time derivative of a quaternion
Discretize the derivative

## Slide 12: Outline
Introduction
Model
Preprocessing and implementation of EKF

## Slide 13: Simple model
The unknown states are the quaternion components. We want to estimate them in order to obtain the object attitude which we do not measure (4-d vector)
Input: gyroscope measurements (3-d vector)
Outputs: accelerometers and magnetometer measurements (6-d vector)

## Slide 14: Model state space equations

## Slide 15: Linearization – state space matrix

## Slide 16: Linearization – input matrix

## Slide 17: Linearization – Output matrix

## Slide 18: Outline
Introduction
Model
Preprocessing and implementation of EKF

## Slide 19: Steps
Check sensors frames on the smarthpone
Acquire static measurement to compensate for biases in the sensors
Calibrate magnetometer
Implement the code